## Slide 1: BUREAU OF FIRE PROTECTION MAKATI CITY FIRE STATION
Fire and Life Safety Seminar
WELCOME !
PARTICIPANTS

## Slide 2: OBJECTIVE OF SEMINAR
To acquire basic knowledge on the nature and behavior of fire
To be familiar with the proper response procedures during fire emergencies
To increase awareness on fire safety and be more prepared in case of a fire incident.

## Slide 3: COURSE OUTLINE
BFP HISTORY
NATURE AND BEHAVIOR OF FIRE
CLASSES OF FIRE
PARTS & USE OF FIRE EXTINGUISHER
ORGANIZATIONAL STRUCTURE OF FIRE BRIGADE
FIRE EVACUATION DRILL & PROCEDURE
FIRE EMERGENCY PROCEDURE
PERSONAL PROTECTIVE EQUIPMENT
BASIC FIRE SAFETY FEATURES IN A BUILDING
FIRE SAFETY TIPS

## Slide 4: Bureau of Fire Protection
Through the enactment of the RA 6975,also known as the DILG Act of 1990, the Fire Service was separated from the PC-INP as a separate and distinct agency as Bureau of Fire Protection on August 2, 1991.
BFP is mandated to prevent and suppress destructive fires, conduct investigation, provide emergency medical and rescue services and enforce the Republic Act 9514.

## Slide 5
The Revised Fire Code of the Philippines
and its Implementing Rules and Regulations
(R.A. 9514)
Fire Safety Inspections
Fire Safety Seminar
Fire Drills
Fire Brigade for establishments employing at least 50 persons

## Slide 6
Fire – The active principle of burning, characterized by the heat and light of combustion (RA 9514). It is a rapid oxidation process accompanied with the evolution of light and heat of varying intensities

## Slide 7
The Tetrahedron of Fire
Oxygen Sources
Approximately 16% Required
Normal air contains 21% O2. Some fuel materials contain sufficient oxygen within their makeup to support burning.
Heat Sources
To Reach Ignition Temperature
Open Flames - The Sun
Hot Surfaces
Sparks and Arcs
Friction - Chemical Action
Electrical Energy
Compression of Gases
GAS
Natural Gas Propane
Butane Hydrogen
Acetylene
Carbon Monoxide
LIQUID
Gasoline Kerosene
Turpentine Alcohol
Liver Oil Paint
Varnish Lacquer
Olive Oil Others
SOLID
Bulky - Dust
Finely Divided Coal
Wood Paper
Cloth Plastic
Grain Others
CHEMICAL
REACTION

## Slide 8
STAGES
OF FIRE

## Slide 9
IGNITION STAGE
  Point wherein the fire starts
  There is plenty of oxygen, little heat and smoke
  Fire is still small and generally confined to the fuel that initially ignited

## Slide 10
GROWTH STAGE
  Temperature and smoke level increases
  Oxygen level decreased and the fuel is already dried out
  Hot gasses rise to the ceiling and spreads outward the walls
  Can be continuous if there is enough fuel and oxygen
  The smoke layer is getting thicker and fire is starting to spread to nearby furniture

## Slide 11
FLASH OVER
  Transition between growth and fully developed stage
  Presence of huge smoke which indicates the rapid change of situation
  May involve exposed combustibles
  Increasing level of smoke with decreased visibility
  Gasses are generated by heat

## Slide 12
FULLY DEVELOPED
All combustibles materials present are continuously burning
Maximum amount of heat is released
The volume of fire is dependent of the number and size of ventilation openings
Unburned gasses begin flowing to adjacent spaces and ignite once it enters a space where air more abundant

## Slide 13
DECAY
Intensity of fire decreasing due to lack of available fuel
Most of fuel consumed
Effort concentrated on cooling of the remaining fuel

## Slide 14
METHODS OF
HEAT TRANSFER
By Radiation
By Convection
By Conduction
By Direct Contact

## Slide 15
Radiation
Radiation is the transmission of heat energy through electromagnetic wave.

## Slide 16
Convection
Convection is the transfer of heat energy by the movement of heated fluids.
HEAT

## Slide 17
M
E
T
A
L
Ordinary combustible materials
M
E
T
A
L
Heat Transfer by Conduction. It is the transmission of heat from one body to another. It is the transfer of heat from one molecule to another molecule

## Slide 18
Fire Extinguishment Theory
Cooling-temperature reduction
Smothering-oxygen dilution
Fuel Removal
Inhibition-breaking the chemical
reaction

## Slide 19
REDUCTION OF HEAT
1. Use something that absorb heat
2. Use water being the best cooling agent
3. Use foam which contains 94% water

## Slide 20
. EXCLUSION OR DEPRIVATION OF OXYGEN
Secure the door at close position
Displacement or diluting oxygen by means of CO2
Blanketing- using wet blanket as foam

## Slide 21
REMOVAL OF FUEL
Shut off fuel supply
Relocate flammable/ combustible materials

## Slide 22
INHIBITION OF CHAIN REACTION or breaking
the combustion Chain

## Slide 23
Classification of Fire
A fire is classified according to the fuel it consumes
CLASS A
Ordinary combustibles or fibrous material, such as wood, paper, cloth, rubber and some plastics.

## Slide 24
CLASS B
Flammable or combustible liquids such as gasoline, kerosene, paint, paint thinners and propane.
CLASS C
Energized electrical equipment, such as appliances, switches, panel boxes and power tools.

## Slide 25
CLASS D
Certain combustible metals, such as magnesium, titanium, potassium and sodium. They may react violently with water or other chemicals, and must be handled with care.
CLASS K
Fires involving combustible cooking fluids such as oils and fats.

## Slide 26
Fire Extinguisher
-is a handy, first aid fire fighting equipment
FIRST AIDE FIRE FIGHTING APPLIANCE

## Slide 27: Fire Extinguisher Anatomy
DISCHARGE HOSE
DISCHARGE NOZZLE
DISCHARGE ORIFICE
BODY
DATA PLATE
CARRYING
HANDLE
PRESSURE GAUGE
(not found on CO2
extinguishers)
DISCHARGE LEVER
DISCHARGE LOCKING PIN
AND SEAL
Notes: POINT OUT DIFFERENT COMPONENTS OF PORTABLE FIRE EXTINGUISHER.
POINT OUT THAT CO2 EXTINGUISHER IS UNIQUE IN THAT IT DOES NOT HAVE PRESSURE GAUGE.

## Slide 28
P – Pull the pin
A – Aim the nozzle
S – Squeeze the lever
S – Sweep side to side at the
base of the fire
HOW TO USE A FIRE EXTINGUISHER

## Slide 29
Classifications of Fire Extinguishers

## Slide 30
Hexafluoropropane HFC-236fa (FE-36)
- Clean Agent
an environmentally preferred alternative to Halon with zero-Ozone Depleting Potential (ODP);
Montreal Protocol & RA 8749 (aka The Philippine Clean Air Act) compliant
Recommended for A, B and C Types of fire

## Slide 31
Dry Chemical
Today’s most widely used type of fire extinguisher is the multipurpose dry chemical that is effective on Class A, B and C fires. This agent also works by creating a barrier between the oxygen element and the fuel element on Class A fires.

## Slide 32
Aquaeuos Film Forming Foam (AFFF)
This type of fire extinguisher puts out the fire by taking away the heat element of the fire triangle. Foam agents separate the oxygen element from the other elements
Water extinguishers are for Class A fires only – although they can sometimes be used on Class B fires. The discharge stream could spread the flammable liquid in a Class B fire if the mixture of the fire agent is inaccurate, or could create a shock hazard on a Class C fire.

## Slide 33
Wet Chemical is a new agent that extinguishes the fire by removing the heat of the fire triangle and prevents re-ignition by creating a barrier between the oxygen and fuel elements.
Wet Chemical or Class K extinguishers were developed for modern, high efficiency deep fat fryers in commercial cooking operations. Some may be used on Class A fire in commercial kitchens.
Dry Powder extinguishers are similar to dry chemical except that they extinguish the fire by separating the fuel from the oxygen element or by removing the heat element of the fire triangle.
However, dry powder extinguishers are for Class D or combustible metal fires only. They are ineffective on all other classes of fires.

## Slide 34: FIRE DRILL
is an exercise or practice that teach the people on how to leave the building safely.
∞PURPOSE OF FIRE DRILL:
1. Ensure the efficient and safe of exits
2. Help prevent panic
3. Occupants participating in a drill learns to:
a. locate the fire exits of the building
b. leave the building/house in a smooth, safely, orderly and
disciplined manner
c. recognize or familiarize the actual sound of the fire alarm
system
d. assemble at the designated evacuation area

## Slide 35
FIRE BRIGADE
ORGANIZATION

## Slide 36
Fire Brigade Chief
Communication Team
Fire Fighting Team
Evacuation Team
Security & Traffic Team
Rescue & Salvage Team
Floor Captain / Safety Officer
Fire Safety Personnel
Deputy Fire Brigade Chief
First Aid Team
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
Floor Marshal
FIRE BRIGADE ORGANIZATIONAL STRUCTURE
1st
2nd
3rd
4th
5th
6th
7th
8th
9th
10th
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)
Evac Guide (2)

## Slide 37: `
Bureau of Fire Protection
Makati City Fire Station
Fire Marshal (FM)
During emergencies, the FM should have a complete monitoring and supervision of the situation
The FM must be able to immediately set up a Command Post
The FM must immediately have an available copy of the floor plan/lay out of the building
The FM should regularly organize fire safety seminars and drills for the building fire brigade and occupants

## Slide 38
Assistant Brigade Marshal (ABM)
During an emergency, the ABM should take charge of the situation in the absence of the BM
Must provide full assistance to the BM on the supervision of fire brigade
Communication Team
Upon confirmation that fire is positive, the assigned communication team must immediately call the nearest fire station or any provided emergency hotline
Must be always prepared to give public address in case of evacuation

## Slide 39
Firefighting Team
Must have at least 4 members to act as Nozzle man, Back-up, Line man and Valve operator
Upon verification of a reported fire, the first responders (2 persons) must bring 2 fire extinguishers and a handheld radio
They are responsible in immediately informing the BM/Communication team if the fire is positive
Must be able to provide quick assessment if the fire is uncontrollable

## Slide 40
Evacuation Team
Must have atleast 2 members per floor
They are responsible for providing full assistance on the proper evacuation of all the occupants of the building
Should be familiar with all the entry and exit points of the building including the designated evacuation area

## Slide 41
Security/Traffic Team
All security personnel are automatically designated as Security/Traffic team members
Should know the roles/responsibilities of ALL the fire brigade members
During a fire emergency, 1 security personnel must serve as a fireman’s guide and assist the responding BFP personnel on the exact location of the fire scene

## Slide 42
Security/Traffic Team
The team must ensure the safety of the evacuation area and assist the police in crowd control
All the members are required to be familiar with the lay-out of the building giving much emphasis on the location of the utility rooms and/or tenants storing high hazard equipment (i.e server rooms)

## Slide 43
Rescue Team
Once the evacuation signal/alarm is sounded, the rescue team shall conduct initial search & rescue procedures on the building
Must immediately bring the victims at the designated first aid station
Salvage Team
During a fire emergency, the salvage team is responsible for saving savable properties within the fire scene or those properties that can be saved from further damage to lessen the amount of damages

## Slide 44
First Aid Team
Responsible for the proper and immediate application of Basic First Aid to the victims
Must monitor the hospitals wherein the victims were brought
Should be properly trained in Basic First Aid and CPR

## Slide 45
Fire Safety Personnel
Responsible for the daily monitoring and inspection of all the fire safety features of the building
In case the sprinkler system activates during a fire incident, they must be on stand-by on the involved isolation valve for an immediate shut-off after the declaration of FIRE OUT by BFP

## Slide 46: A Fire Brigade must remember to:
Determine the Specific Fire Floor
Begin the Control of Evacuation
Search of the fire floor and all floors above the fire
Gain Control of Building Systems
Confine and Extinguish the Fire

## Slide 47
IN CASE OF FIRE
Proceed to the designated evacuation area
Immediately leave the building by means of nearest available exit
Notify other persons on your way out
Never go back to the burning building
REMAIN CALM, THINK AND ACT!

## Slide 48
During a Fire Emergency, there should be a:
1. Command Post (FM, Tech Staff)
-White Board
-Floor/Key Plan of the building
-Radio
2. First Aid Station
3. Evacuation Area
4. Caution Tape

## Slide 49
Basic Information for the white board:
Time fire started:
Floor/s involved/Location:
Time of call to the Fire Dept:
Time Evacuation started:
Time Responder/s arrived:
Time Evacuation ended:
Time of fire out:
Name of victim/s | Type of injury | Responding Ambulance | Recipient hospital

## Slide 50
PERSONAL PROTECTIVE EQUIPMENT

## Slide 51
Helmet
Bunker/Fire coat

## Slide 52
Trouser
Suspenders

## Slide 53
Gloves
Fire Boots

## Slide 54: BASIC FIRE SAFETY FEATURES OF A BUILDING
Automatic Fire Suppression System-Sprinkler System
Fire Hose Cabinet
Fire Detection and Alarm System-Smoke detectors
Means of Egress (Emergency Exit)
Portable Fire Extinguishers

## Slide 55
Fire Safety Tips

## Slide 56
Identify and report fire hazards and unsafe work practices.
Unplug all electrical equipment when not in operation, unless necessary.
Maintain proper housekeeping
Familiarize and keep emergency exits marked, lighted and free from any obstruction.

## Slide 57
5. Familiarize location of fire alarm, fire extinguishers and other fire fighting equipment.
6. Enforce “No Smoking” policy
7. Avoid overloading of electrical circuits by plugging many appliances

## Slide 58
8. Do not store large volume of combustible
liquids without proper clearance/permit and
fire protection
9. Ensure complete attendance of ALL fire
brigade members during Fire Safety Seminars
and Drills
10.Regularly conduct emergency drills (internal)

## Slide 59
IN CASE OF FIRE
Should you discover
Fire/Medical Emergency
Call 168
Or
818 5150

## Slide 60
FIRE BRIGADE
ORGANIZATION
FIRE FIGHTING TEAM
MEDICAL TEAM
COMMUNICATION TEAM
SECURITY TEAM
SEARCH and RESCUE TEAM
EVACUATION and SALVAGE TEAM
FIRE MARSHAL
End of
Presentation
THANK YOU!
LIKE US ON FACEBOOK @ Makati City Fire Station